## Slide 1
Wifi Training - Hands On
Brazil Application
FW 3.4

## Slide 2: Labs Prerequisites
Hardware
  NUCLEO-F401
  X-NUCLEO-IDW01M1
Utility software
  Tera Term: terminal emulator (available from http://en.sourceforge.jp/projects/ttssh2/releases)
  Text Editor
  Web browser
  CubeMX
  ODE firmware
  CubeMX wifi: en.x-cube-wifi1_firmware.zip
2

## Slide 3: STM32 Open Development Environment Fast, affordable Prototyping and Development
The STM32 Open Development Environment (ODE) consists of a set of stackable boards and a modular open SW environment designed around the STM32 microcontroller family.
www.st.com/stm32ode
Compatibility with multiple Development environments
STM32Cube development software
STM32 Nucleo expansion boards
STM32 Nucleo development boards
STM32Cube expansion software

## Slide 4: STM32 Nucleo Development Boards (NUCLEO)
Power supply through USB or external source
Integrated debugging and programming ST-LINK probe
STM32 microcontroller
Complete product range from ultra-low power to high-performance
ST morpho extension header
A comprehensive range of affordable development boards for all the STM32 microcontroller series, with unlimited unified expansion capabilities and integrated debugger/programmer functionality.
www.st.com/stm32nucleo
Arduino™ UNO R3 extension headers

## Slide 5: STM32 Nucleo Expansion Boards (X-NUCLEO)
Move/Actuate
Power
Interact
Connect
Sense
Boards with additional functionality that can be plugged directly on top of the STM32 Nucleo development board or stacked on another expansion board.
DIL24 support for new devices
Motion MEMS sensors
Environmental sensors
www.st.com/x-nucleo
Example of STM32 expansion board (X-NUCLEO-IKS01A1)

## Slide 6: STM32 Open Development Environment Building block approach
The building blocks
Your need
Our answer
Move / Actuate
Connect
Power
Sense
Process
Inertial modules, magnetometer
Proximity, microphone
Pressure, temperature, humidity
Bluetooth LE, Sub-GHz radio
NFC, Wi-Fi, GNSS
Energy management & battery
General-purpose microcontrollers
Stepper motor driver
DC & BLDC motor driver
Audio amplifier
COLLECT
TRANSMIT
ACCESS
CREATE
POWER
PROCESS
Software
Secure microcontrollers
Touch controller
Operation Amplifier
Accelerometer, gyroscope
Translate
Industrial input / output
www.st.com/stm32ode

## Slide 7: Connectivity: SPWF01S – Wi-Fi modules
2.4 GHz IEEE 802.11 b/g/n low power transceiver
STM32 ARM Cortex-M3 microcontroller
Integrated high gain antenna or u.fl connector
Pre Certified RF (FCC, IC, CE, SRRC)
1.5 MB or 512 kB Integrated Flash memory
Integrated TC/IP and Application Layer Functions
Easy interface to host Microcontroller through UART and AT commands set
TLS 3.0/SSL 1.2 for End to End security integrated
System Modes: Mini-AP, IBSS and Station
Built-in Application: Sockets, Web Server, Rest API
Over The Air firmware and external flash update
Easy configuration (SSID, PWD) in miniAP
Small form factor: 26.92 x 15.24 x 2.35 mm
Integration
Flexibility and ease of use
RF power
Size
Up to +18 dBm output power
The SPWF01S is a “Cloud Compatible” Wi-Fi Modules embedding all the FW e.g. TLS/SSL security, Rest API, to easily connect Sensors and Actuators to Remote Cloud Services
www.st.com/wifimodules
SPWF01SC Integrated U.FL connector
SPWF01SA Integrated antenna

## Slide 8: Wi-Fi expansion board (X-NUCLEO-IDW01M1) Hardware Overview (1/3)
X-NUCLEO-IDW01M1 Hardware Description
TheX-NUCLEO-IDW01M1 is a Wi-Fi evaluation board based on the SPWF01SA module, which expands the STM32 Nucleo boards. The CE, IC and FCC certified SPWF01SA module has an embedded STM32 MCU, a low-power Wi-Fi b/g/n SoC with integrated power amplifier and power management and a SMD antenna. The SPWF01SA module communicates with the STM32 Nucleo developer board host microcontroller though an USART link available on the Arduino UNO R3 connectors.
Main Features
X-NUCLEO-IDW01M1 hosts FCC, IC and CE certified SPWF01SA module (FCC ID: VRA-SG9011203, IC: 7420A-SG9011203 and ETSI compliant)
SPWF01SA module major characteristics
compatible with STM32 Nucleo boards
equipped both with ST-morpho and Arduino UNO-R3 connectors
scalable solution; it can cascade multiple boards for larger systems
free development firmware library and examples, compatible with STM32Cube
RoHS compliant
Key Products on board
  SPWF01SA: Wi-Fi module has an embedded STM32 MCU, a low-power Wi-Fi b/g/n SoC with integrated power amplifier and power management and a SMD antenna.
Latest info available at X-NUCLEO-IDW01M1
** Connector for the STM32 Nucleo Board
Order code: X-NUCLEO-IDW01M1
Printed Antenna
Arduino UNO R3 connectors
ST morpho connectors
STM32
Wi-Fi Frontend

## Slide 9: Motion MEMS and environmental sensors expansion board (X-NUCLEO-IKS01A1) Hardware Overview (2/3)
Key Product on board
  LSM6DS0: MEMS 3D accelerometer (±2/±4/±8 g) + 3D gyroscope (±245/±500/±2000 dps)
  LIS3MDL: MEMS 3D magnetometer (±4/ ±8/ ±12/ 16 gauss)
  LPS25HB: MEMS pressure sensor, 260-1260 hPa absolute digital output barometer
  HTS221: capacitive digital relative humidity and temperature
  DIL 24-pin: socket available for additional MEMS adapters and other sensors (UV index)
DIL 24-pin
X-NUCLEO-IKS01A1 Hardware Description
The X-NUCLEO-IKS01A1 is a motion MEMS and environmental sensor evaluation board.
It is compatible with the Arduino UNO R3 connectors layout, and is designed around ST’s latest sensors.
Arduino UNO R3 connector
ST morpho connector**
** Connector for the STM32 Nucleo Board
HTS221
LPS25HB
LSM6DS0
LIS3MDL
Latest info available at
X-NUCLEO-IKS01A1
Order code: X-NUCLEO-IKS01A1

## Slide 10: NFC expansion board (X-NUCLEO-NFC01A1) Hardware Overview (3/3)
X-NUCLEO-NFC01A1 Hardware Description
The X-NUCLEO-NFC01A1 is a Dynamic NFC tag evaluation board designed around the M24SR64-Y that allows expansion of the STM32 Nucleo boards.
The M24SR64-Y communicates with STM32 Nucleo developer board though an I2C link available on the Arduino UNO R3 connector
Arduino UNO R3 connector
Key Products on board
  M24SR: This device is dynamic NFC/RFID tag IC with a dual interface. It embeds a 64 Kbit EEPROM memory. It can be operated from an I2C interface or by a 13.56 MHz RFID reader or a NFC Smartphone.
  NFC antenna: 31 mm x 30 mm 13.56 MHz double layer inductive antenna etched on the PCB (ANT14)
Latest info available at X-NUCLEO-NFC01A1
M24SR
Printed Antenna
Order code: X-NUCLEO-NFC01A1

## Slide 11: FP-CLD-BLUEMIX1 Software Overview
FP-CLD-BLUEMIX1 Software Description
FP-CLD-BLUEMIX1 is an expansion software package for STM32Cube for portability across different STM32 microcontrollers. The software runs on the STM32 microcontroller and includes drivers for the SPWF01SA Serial-to-Wi-Fi module, HTS221, LPS25HB, LSM6DS0, LIS3MDL sensors, and M24SR64-Y dynamic NFC/RFID tag. It also includes a middleware package implementing the MQTT protocol over TLS 1.2 is used as application protocol to facilitate interaction between the STM32 Nucleo boards and Cloud services and securing data. The software includes examples for visualizing sensor data and controlling the device via IBM Bluemix® Cloud service.
Key features
  Complete middleware to build applications based on Wi-Fi connectivity (SPW01SA) and to connect STM32 Nucleo boards with Cloud based services
  Software interface to access temperature and humidity sensor (HTS221), pressure sensor (LPS25HB), motion sensors (LIS3MDL and LSM6DS0) and to write and read the RFID/NFC tag (M24SR64-Y)
  Integrated MQTT protocol middleware
  Sample implementation available on board X-NUCLEO-IKS01A1, X-NUCLEO-IDW01M1, and X-NUCLEO-NFC01A1, when both connected to NUCLEO-F401RE
  Easy access to IBM Bluemix® Cloud services for sensors data visualization and processing
  Easy portability across different MCU families, thanks to STM32Cube
  Free, user-friendly license terms
Overall Software Architecture
FP-CLD-BLUEMIX1
Latest SW available at
Hardware Abstraction Layer API
Boards Support Packages
Drivers
Development boards
X-NUCLEO-IDW01M1
Expansion Board
STM32 Nucleo Board
Wi-Fi Middleware
Middleware
CMSIS
Utilities
HW Components
STM32
SPWF01SA
Applications
IBM Bluemix Application
X-NUCLEO-IKS01A1
Expansion Board
HTS221
LPS25HB
LSM6DS0
LIS3MDL
MQTT
X-NUCLEO-NFC01A1
Expansion Board
M24SR64
NFC Middleware
For IBM Bluemix package: www.st.com/web/catalog/tools/FM147/CL1794/SC961/SS1743/LN1992/PF263214
Notes: MQTT: MQ Telemetry Transport

## Slide 12: Documents & Related Resources
FP-CLD-BLUEMIX1: Product Folder (Link)
  DB2819: Connectivity to the IBM Bluemix® Cloud with Wi-Fi, NFC and sensors software expansion for STM32 Cube – data brief
  UM2007: Getting started with the software package for Wi-Fi, NFC and sensors for connectivity with IBM Bluemix® Cloud in FP-CLD-BLUEMIX1 – user manual
X-NUCLEO-IDW01M1: Product Folder (Link)
  Gerber files, BOM, Schematic
  DB2726: Wi-Fi expansion board based on SPWF01SA module for STM32 Nucleo – data brief
  UM1975: Getting started with X-NUCLEO-IDW01M1 Wi-Fi expansion board based on SPWF01SA module for STM32 Nucleo – user manual
X-NUCLEO-IKS01A1: Product Folder (Link)
  Gerber files, BOM, Schematic
  DS10619: Motion MEMS and environmental sensor expansion board for STM32 Nucleo – data brief
  UM1820: Getting started with motion MEMS and environmental sensor expansion board for STM32 Nucleo – user manual
X-NUCLEO-NFC01A1: Product Folder (Link)
  Gerber files, BOM, Schematic
  DB2353: Dynamic NFC tag expansion board based on M24SR for STM32 Nucleo – data brief
  AN4624: Getting started with the STM32 Nucleo and the M24SR expansion board X-NUCLEO-NFC01A1 – application note
  UM1793: Dynamic NFC tag expansion board based on M24SR for STM32 Nucleo – user manual
All documents are available in the Design Resources tab of
the FP-CLD-BLUEMIX1 Webpage

## Slide 13: Hands on Agenda
3
Lab 1: HW and SW setup
Lab 2: Set the SPWF variables
Lab 2a: FOTA update
Lab 3: Access point connection (WPA or WEP)
Lab 4: Web client mode
Lab 5: Web server mode – files in RAM
Lab 6: Web server mode – files in FLASH
Lab 7: Socket interface
Lab 8: MiniAP mode for the first set
Lab 9: Socket interface in MiniAP mode
Lab 10: Web server in MiniAP mode
Lab 11: Remote control of GPIO interfaces
Lab 12: Input demo
Lab 13: Socket Server
Lab 14: Low Power Modes
Lab 15: HW switch from STA to MiniAP
Lab 16: IBSS mode
Lab 17: BlueMIX

## Slide 14: Lab 1: HW and SW setup
Objective
  Hardware set-up
  Software set-up
Prerequisites
  Work alone
4

## Slide 15: Lab 1: EVAL of the SPWF01SA.11 module
5
Plug&Play Solution
AT command set
Power Supplied via the USB interface
UART/USB bridge from Silicon Lab requires to install the correspondent driver on your PC
SMD antenna and reset button on-board
HyperTerminal or similar
AT Commands/Events
VCOM
SWPF01SA
Arduino UNO R3 connector
ST Morpho connector**

## Slide 16: Tutorial #1a: Loading the VCOM driver
Run STM32-Link Utility.
Select “Target” + “Connect”.
Select “Program…”
“Start Address” is 0x08000000.
Select “Project-VCOM-WiFi-STM32F401.bin” in the “NUCLEO-STM32F401 Binaries” subdirectory using “Browse” button.
Click “Start”

## Slide 17: Tutorial #1a: Loading the VCOM driver
Wait for green “Memory programmed…” message.
Select “Target” + “Disconnect”
Done!
Using Teraterm, on the PC, we will now access the SPWF01S module directly over the UART.

## Slide 18: Tutorial #1a: Configuring TeraTerm
Run TeraTerm.
Select “Setup” + “Serial Port…”
Set “Port: to the last COM port.
Set “Baud rate” to “115200”.
Add the delay
Click “OK”.

## Slide 19: Tutorial #1b: Configuring TeraTerm
Configure the Tera Term New-line to receive in AUTO and to Transmit with CR+LF

## Slide 21: Tutorial #1c: Configure the module to echo
Enter: “at”<cr>.
To enable character echo, enter: “at+s.scfg=localecho1,1”<cr>
Enter: “at”<cr>.
Enter: “at&v”<cr>.

## Slide 22: Lab 1: Configuring the UART
Open Tera Term
Command Mode
  Type AT followed by a carriage return (CR)
10
Tera Term output
All | 
OK | 

## Slide 23
You are ready to use your Wifi
EVAL board!

## Slide 24: Lab 2: Set the SPWF variables
Objective
  Run a command
  Get the default configuration dump
  Set host name
  Set static IP parameters
  Reset the module
Prerequisites
  Work alone
12

## Slide 25: Lab 2: Run a command
Run a command - Syntax
AT&x <CR>
AT+S.[Command] <CR>
AT Command Prefix
Response - Syntax
xxxxxxxx
13
OK
Command output followed by OK
ERROR: Command not found
ERROR: Unrecognized key
Not case sensitive

## Slide 26: Lab 2: Set the SPWF variables
Get the default configuration dump
  Type AT&V
Get a variable value
  Type AT+S.GCFG=console1_speed
Config dump frame
14
Variable Name
Variable Value
How to change the variable value?
AT+S.SCFG=[var name],xxxx
AT&W

## Slide 27: Lab 2: Set the SPWF variables
Get the default configuration dump
Set host name
  Type AT+S.SCFG=ip_hostname,xxxxxxxx
15
Up to 31 characters (case sensitive),
͞spaĐeďar͟ is allowed
Tera Term output
All | 
OK | 

## Slide 28: Lab 2: Set the SPWF variables
Get the default configuration dump
Set host name
Set IP address, IP default gateway, IP DNS and IP netmask (for static usage)
  Type AT+S.SCFG=ip_ipaddr,192.168.0.1xx
• Type AT+S.SCFG=ip_gw,192.168.0.1
Type AT+S.SCFG=ip_dns,192.168.0.1
Type AT+S.SCFG=ip_netmask,255.255.255.0
16
Tera Term output
All | 
OK | 

## Slide 29: Lab 2: Set the SPWF variables
Tera Term output
Reset the module
  Type AT+CFUN=1
Get the default configuration dump
Set host name
Set IP address, IP default gateway, IP DNS and IP netmask (DHCP off)
Save settings on the flash memory (mandatory after a variable change)
  Type AT&W
17
All | 
+WIND:21:WiFi Scanning +WIND:35:WiFi Scan Complete (0x0) | 

## Slide 30: Lab 2: Set the SPWF variables
Get the default configuration dump
Set host name
Set IP address, IP default gateway, IP DNS and IP netmask (DHCP off)
Save settings on the flash memory (mandatory after a variable change) and reset the module
Check the new configuration dump
  Type AT&V
18

## Slide 31
Proceed to the next LAB!

## Slide 32: Lab 2a: FOTA update
Objective
  Upgrade the FW using the OTA file
Prerequisites
  OTA file (provided in the SPWF01S FW
package)
  External web server (i.e. Apache web server running on PC)
20

## Slide 33: Lab 2a: FOTA update
21
The SPWF01Sx.11 module (with external flash on board) allows performing a Firmware Over-the-air update via a single HTTP GET.
The SPWF01S will validate the firmware image it downloads, load it into a staging area, then prompt the user to issue a reset command in order to complete the update.

## Slide 34: Lab 2a: FOTA update
The Apache Web Server will be used in this LAB
(Apache Web Server is available at this link: http://archive.apache.org/dist/httpd/binaries/win32/httpd-2.2.25-win32-x86-openssl-0.9.8y.msi)
Note: please check that the local firewall is disabled or properly set. It can block the connection from module to Apache.
Copy the OTA file (i.e. SPWF01S-xxxxxx-yyyyyyy- RELEASE-main.ota) in the Apache 2.2 htdocs folder
22

## Slide 35: Lab 2a: FOTA update
The FWUPDATE command allows to perform a Firmware Over-the- air update via a single HTTP GET.
Sintax
  AT+S.FWUPDATE=<hostname>,<path>,<port>
Configuration parameters
<hostname>
Target host. DNS resolvable name or IP address
<path&queryopts>
<port>
Document path and optional query arguments
Target host port
23

## Slide 36: Lab 2a: FOTA update
The module and the Apache Web server must be connected to the same network
In Tera Term: type AT+S.FWUPDATE=[Apache IP address],/[ota_file.ota]
i.e. type AT+S.FWUPDATE=192.168.x.yyy,/SPWF01S-150410-c2e37a3-RELEASE-
main.ota
Reset the module to apply the new FW
  Type AT+CFUN=1
Restore factory default settings (mandatory)
  Type AT&F
24
Tera Term output
All | 
Staging F/W update for 'SPWF01SX.11' version '1203- 120918_01' F/W length 276824 @ 0x00002800 (offset 0x00000000, block len 4096) Write len 4096 -> 0x0 Write len 4096 -> 0x1000 (note - deleted extra output for clarity) Write len 4096 -> 0x42000 Write len 2476 -> 0x43000 (final) Wrote 276904 bytes Complete! Update will be applied on next reboot. (at+cfun=1) | 

## Slide 37
Proceed to the next LAB!

## Slide 38: Lab 3: Access point connection
Objective
  Scan for available networks
  Join a network
  Check the status/statistics variables
Prerequisites
  USB dongle and computer are set up as described in Lab 2
  Work alone
26

## Slide 39: Lab 3: Scan for available networks
The SCAN command performs an immediate scan for available networks. Infrastructure (AP) and IBSS (Ad-Hoc) networks are both reported. Network type, Channel, BSSID, SSID, Signal strength (RSSI), and 802.11 capabilities are all reported.
Type AT+S.SCAN
(AT+S.SCAN=a,r to perform a non-filtered scan)
27
FOUND: BSS 14:D6:4D:24:36:00 CHAN: 01 RSSI: -28 SSID: 'ENG-WPA' CAPS: 0431 WPA WPA2 FOUND: BSS 00:18:0A:31:EA:78 CHAN: 11 RSSI: -82 SSID: 'ZyckoItalyWireless' CAPS: 0531 WPA WPA2 FOUND: BSS 06:18:0A:31:E7:E2 CHAN: 11 RSSI: -85 SSID: 'ZyckoItalyGuest' CAPS: 0531 WPA WPA2
OK
All
Network type
Network MAC
Network channel
Network RSSI
Network SSID
Network capabilities
Tera Term output

## Slide 40: Lab 3: Joining a network (WPA Key)
Tera Term output
In order to be connected to an available Wifi network, the AP parameters setting is needed.
Set the SSID
  Type AT+S.SSIDTXT=ST_OFFICE
Set the password
  Type AT+S.SCFG=wifi_wpa_psk_text,stbrasil2016
Set the network privacy mode (0=none, 1=WEP, 2=WPA-Personal (TKIP/AES) or WPA2-Personal (TKIP/AES))
  Type AT+S.SCFG=wifi_priv_mode,2
Set the network mode (1 = STA, 2 = IBSS, 3 = MiniAP)
  Type AT+S.SCFG=wifi_mode,1
28
All | 
OK | 

## Slide 41: Lab 3: Joining a network (WPA Key)
ENG-WPA
Save the settings on the flash memory and reset the module
  Type AT&W
  Type AT+CFUN=1
Tera Term output
29
AP
All | 
+WIND:0:Console active +WIND:46:WPA: Crunching PSK... +WIND:32:WiFi Hardware Started +WIND:21:WiFi Scanning +WIND:35:WiFi Scan Complete (0x0) +WIND:19:WiFi Join: 14:D6:4D:24:36:00 +WIND:25:WiFi Association with 'ENG-WPA' successful +WIND:51:WPA Handshake Complete +WIND:24:WiFi Up: 192.168.0.1xx | 

## Slide 42: Lab 3: Joining a network (WPA Key)
Check the status/statistics variables
  Type AT+S.STS
Send a ping to the gateway (ip_gw)
• Type AT+S.PING=192.168.0.1
30
ENG-WPA
AP
Tera Term output
All | 
OK | 

## Slide 43: Lab 3: Joining a network (WEP Key)
Configure the module using the WEP key (4 possible combinations
available)
Sample table:
31
AP configuration | AT command to be used
Security Mode: WEP WEP Key Length: 64 bit (10 hex digits) Authentication: Open Wep Key 1: 1234567890 | i.e. at+s.ssidtxt=ENG-WEP AT+S.SCFG=wifi_wep_keys[0],1234567890 AT+S.SCFG=wifi_wep_key_lens,05 AT+S.SCFG=wifi_auth_type,0 AT+S.SCFG=wifi_priv_mode,1 AT+S.SCFG=wifi_mode,1 at&w at+cfun=1
Security Mode: WEP WEP Key Length: 64 bit (10 hex digits) Authentication: Shared Key Wep Key 1: 1234567890 | i.e. at+s.ssidtxt=ENG-WEP AT+S.SCFG=wifi_wep_keys[0],1234567890 AT+S.SCFG=wifi_wep_key_lens,05 AT+S.SCFG=wifi_auth_type,1 AT+S.SCFG=wifi_priv_mode,1 AT+S.SCFG=wifi_mode,1 at&w at+cfun=1
AP configuration | AT command to be used
Security Mode: WEP WEP Key Length: 128 bit (26 hex digits) Authentication: Open Wep Key 1: 123456789012345678 90123456 | i.e. at+s.ssidtxt=ENG-WEP AT+S.SCFG=wifi_wep_keys[0],12345678 901234567890123456 AT+S.SCFG=wifi_wep_key_lens,0D AT+S.SCFG=wifi_auth_type,0 AT+S.SCFG=wifi_priv_mode,1 AT+S.SCFG=wifi_mode,1 at&w at+cfun=1
Security Mode: WEP WEP Key Length: 128 bit (26 hex digits) Authentication: Shared Key Wep Key 1: 123456789012345678 90123456 | i.e. at+s.ssidtxt=ENG-WEP AT+S.SCFG=wifi_wep_keys[0],12345678 901234567890123456 AT+S.SCFG=wifi_wep_key_lens,0D AT+S.SCFG=wifi_auth_type,1 AT+S.SCFG=wifi_priv_mode,1 AT+S.SCFG=wifi_mode,1 at&w at+cfun=1

## Slide 44: Lab 3: Joining a network (WEP Key)
Notes:
“wifi_wep_key_lens” variable values: 05 and 0D
It’s possible to enter any text string into a WEP key box in the AP, in which case it will be converted into a hexadecimal key using the ASCII values of the characters. A maximum of 5 text characters can be entered for 64 bit keys, and a maximum of 13 characters for 128 bit keys.
In this case, it needs to manually convert your ASCII password to HEX and complete the wifi_wep_keys[0] variable with the HEX value.
i.e.
AP WEP key: test1
ASCII to HEX: 74:65:73:74:31
So, the AT command is: AT+S.SCFG=wifi_wep_keys[0],7465737431
32

## Slide 45
Proceed to the next LAB!

## Slide 46: Lab 4: Web client mode
Objective
  HTTP GET
  HTTP POST
  PUSH DATA ON SERIAL PORT
Prerequisites
  USB dongle and computer are set up as described in Lab 2
  Work in couple
34

## Slide 47: Lab 4: HTTP GET
The HTTP GET feature performs a single HTTP request to the specified
host and path. The server response is printed on the UART enabled.
Sintax
  AT+S.HTTPGET=<hostname>,<path>[,<port>]
Configuration parameters
  <hostname>: target host. DNS resolvable name or IP address
  <path>: document path
  <port>: target port
35

## Slide 48: Lab 4: HTTP GET
Device A performs an HTTP GET to the Device B
  Device A:
AT+S.HTTPGET=<Device B IP addr>,/index.html Type AT+S.HTTPGET=192.168.0.1xx,/index.html
Tera Term output
Device A
36
GET /index.html HTTP/1.0 User-Agent: SPWF01S
………..
<h1>ST SPWF01Sx.11 WiFi Module</h1>
<p>
Welcome to the ST SPWF01Sx.11 WiFi Module.
</p>
<p>
This page was delivered from the SPWF01Sx.11 internal HTTP server.
…..
<a href=/status.shtml>SPWF01Sx.11 Status Page</a>
</p>
</body>
</html>
OK
A
B

## Slide 49: Lab 4: HTTP POST
The HTTP POST performs a post of the given path to the specified host.
The module can be only used as an HTTP POST client.
Sintax
  AT+S.HTTPPOST =<hostname>,<path&queryopts>,<formcontent>[,<port>]
Configuration parameters
  <hostname>: target host. DNS resolvable name or IP address
  <path&queryopts>: document path
  <formcontent>: form to be submitted
  <port>: target port
37

## Slide 50: Lab 4: HTTP POST
The SPWF01S performs an HTTP POST to an HTTP Post Test Server
  Type: at+s.httppost=posttestserver.com,/post.php,name=demo&email=mymail&subjec t=subj&body=message
The HTTP Post Test Server replies as displayed in the Tera Term output if the HTTP POST successfully
38
A
B
Tera Term output
HTTP POST SERVER
Device A | 
HTTP/1.1 200 OK Date: Fri, 10 Jan 2014 13:24:14 GMT Server: Apache Access-Control-Allow-Origin: * Vary: Accept-Encoding Content-Length: 139 Connection: close Content-Type: text/html Successfully dumped 4 post variables. View it at http://www.posttestserver.com/data/2014/01/10/0 5.24.1443192628 Post body was 0 chars long. OK | 

## Slide 51: Lab 4: HTTP POST
38

## Slide 52: Lab 4: Push data on serial port
A built-in html page “output_demo.html” allows to remotely push
characters on the serial port from a remote browser.
39
output_demo.html
Module’s IP address/output_demo.html

## Slide 53: Lab 4: Push data on serial port
Find your IP address
  Type AT+S.STS
Associate your computer with the AP
Open your web browser
In the address bar, type
<module’s IP
Address>/output_demo.html
  Type 192.168.0.1xx/output_demo.html
40

## Slide 54: Lab 4: Push data on serial port
Enter the text
Submit
The text will be sent to the serial port of the module
41

## Slide 55
Proceed to the next LAB!

## Slide 56: Lab 5: Web Server use mode
Objective
  List existing files
  Print a file
  Create a file
  Append to an existing file
  Delete an existing file
Prerequisites
  USB dongle and computer are set up as described in Lab 2
  Work alone
43

## Slide 57: Lab 5: Web server
44
The Web Server feature allows to create, print and delete ASCII files in the RAM memory of the module.

## Slide 58: Lab 5: List existing files
The FSL command lists type, sizes and name of all the existing files.
Type AT+S.FSL
45
I 461 /input_demo.shtml
I 180 /message.shtml
I 384 /output_demo.html
I 614 /index.html
I 157 /peers.shtml
I 193 /config.shtml
I 174 /status.shtml
I 212 /404.html
I 2022 /firstset.html
I 2898 /remote.html
OK
All
Files stored in the STM32 FLASH memory
Tera Term output

## Slide 59: Lab 5: Print a file
The FSP command prints the content
of an existing file.
Type AT+S.FSP=/index.html
46
Tera Term output
Tip: How to use the offset and length parameters: AT+S.FSP=/index.html,[offset],[length]
i.e. Type AT+S.FSP=/index.html,5,20
Length parameter is mandatory if is used the offset.
All | 
<html> <head><title>ST SPWF01S</title></head> <body bgcolor="white" text="black"> <h1>ST SPWF01S Intelligent WiFi Module</h1> <p>Welcome to the ST SPWF01S intelligent Wi-Fi module.</p> <p>This page was delivered from the SPWF01S internal HTTP server.</p> <p> <a href=/config.shtml>SPWF01S Configuration Settings Page</a> </p> <p> <a href=/status.shtml>SPWF01S Status Page</a> </p> <p> <a href=/peers.shtml>SPWF01S Peers Page</a> </p> <p>More information about the SPWF01S and other ST products can be found at ST's website: <a href="http://www.ST.com/">http://www.ST.com/</a>.</p> </body> </html> OK | 

## Slide 60: Lab 5: Create a file
The FSC command allows to create a file inside the SPWF for
delivery by the SPWF HTTP server.
Sintax
  AT+S.FSC =<fname>,<max_len>[,<http_header>]
Configuration parameters
  < filename >: filename to create
  < max_len >: amount of space to allocate for file, max = 4096 bytes
  <http_header>: 0=HTML header automatically added, 1=HTML header not added (as by default)
Tera Term output
Type AT+S.FSC=/wifidemo.html,1965
47
All | 
OK | 

## Slide 61: Lab 5: Configuring the UART
Set CR+LF in the Terminal setup (to properly paste text in the terminal):
  Tera Term: Setup → Terminal →
Transmit: CR+LF
48

## Slide 62: Lab 5: Append to an existing file
The FSA command allows to append blocks of data to an existing file.
This command accepts data after the <cr> at the end of the command
line.
Sintax
  AT+S.FSA=/<filename>,<datalen>
Configuration parameters
  < filename >: filename pre-created
  < datalen >: number of characters to append to the file
Type AT+S.FSA=/wifidemo.html,1965
49
Tips
Now SPWF accepts data

## Slide 63: Lab 5: Append to an existing file
Open wifidemo.txt in the following directory: Hands_on folder/HTML_demo_page
Copy the file content into Tera term (paste with ALT+V or mouse right button)
50
Tera Term output
All | 
OK | 

## Slide 64: Lab 5: Append to an existing file
Open wifidemo.html
  Open your Web browser (suggested Google
Chrome for HTML5 test)
  In address bar, type <SPWF IP addr>/wifidemo.html Type 192.168.0.1xx/wifidemo.html
51

## Slide 65: Lab 5: Configuring the UART
Re-set CR in the Terminal setup
as by default
  Tera Term: Setup → Terminal →
Transmit: CR
52

## Slide 66: Lab 5: List existing files
Let's list the files
Type AT+S.FSL
53
D 1965 /wifidemo.html
I 461 /input_demo.shtml
I 180 /message.shtml
I 384 /output_demo.html
I 614 /index.html
I 157 /peers.shtml
I 193 /config.shtml
I 174 /status.shtml
I 212 /404.html
I 2022 /firstset.html
I 2898 /remote.html
OK
All
File stored in the RAM memory
Tera Term output

## Slide 67: Lab 5: Delete an existing file
The FSD command allows to delete an existing file by name. Static
files may not be deleted.
Sintax
  AT+S.FSD=/<filename>
Type AT+S.FSD=/wifidemo.html
54
Tera Term output
All | 
OK | 

## Slide 68: Lab 5: Delete an existing file
Re-open wifidemo.html
  Open your Web browser
  In address bar: <SPWF IP addr>/wifidemo.html Type 192.168.0.1xx/wifidemo.html
55

## Slide 69
Proceed to the next LAB!

## Slide 70: Lab 6: Web Server use mode
Objective
  Create an image file
  Filesystem update over-the-air
Prerequisites
  Work alone
57

## Slide 71: Lab 6: Web server
58
The Web Server feature also allows to upload generic files (PDF, HTML, DOC, JPEG and so on) in the EXTERNAL FLASH memory of the module. It needs to follow the below steps:
create an image file (IMG) using the tool provided in the Hands-on package (the IMG contains the files to upload)
Put the image in a generic and accessible Web Server (Apache Web server
will be used in the Hands-on as example)
Using the proper AT command, the IMG will be retrieved over-the-air and the static files will be created in the external flash memory

## Slide 72: Lab 6: Create an image file
Open the following folder and
extract all the files:
../hands_on_wifi/filesystem_update
Put your own files to upload in the
pages folder (max 512 Kbytes)
Run gen.bat
Open the pages folder and copy outfile.img in your external Web Server (Apache)
3
59
1 2 |  | 

## Slide 73: Lab 6: Create an image file
The Apache Web Server will be used in this tutorial
(Apache Web Server is available at this link: http://archive.apache.org/dist/httpd/binaries/win32/httpd-2.2.25-win32-x86-openssl-0.9.8y.msi)
Note: please check that the local firewall is disabled or properly set. It can block the connection from module to Apache.
Copy outfile.img in the Apache 2.2
htdocs folder (this is the default root server directory)
60
4

## Slide 74: Lab 6: Filesystem update
The HTTPDFSUPDATE command allows to create static files inside the SPWF for delivery by the SPWF HTTP server.
Sintax
  AT+S.HTTPDFSUPDATE=<hostname>,<path>[,port]
Configuration parameters
  <hostname>: external web server. DNS resolvable name or IP address
  <path>: document path
  <port>: target host port
61

## Slide 75: Lab 6: Filesystem update
In Tera Term: type
AT+S.HTTPDFSUPDATE=192.168.x.10x,/outfile.img
Reset the module
  Type AT+CFUN=1
62
Tera Term output
Warning
The file system will be permanently deleted.
The new IMG will overwrite the existent files in the file system
All | 
Image length 357957 (offset 0x00080000, block len 4096) | 
Write len 4096 -> 0x80000 | 
Write len 4096 -> 0x81000 | 
Write len 4096 -> 0x82000 | 
………….. | 
……………… | 
…………… | 
Write len 4096 -> 0xD6000 | 
Write len 1612 -> 0xD7000 (final) | 
Wrote 357964 bytes | 
Complete! Please reboot. (at+cfun=1) | 
OK | 

## Slide 76: Lab 6: Filesystem update
Let's list the files
Type AT+S.FSL
63
Files stored in the EXT FLASH
memory
Tera Term output
All |  | 
 | E 2615 /st766.gif E 112374 /module.png E 2430 /index1.html E 419 /index.html E 239887 /MKTWiFi.pdf I 461 /input_demo.shtml I 180 /message.shtml I 384 /output_demo.html I 614 /index.html I 157 /peers.shtml I 193 /config.shtml I 174 /status.shtml I 212 /404.html I 2022 /firstset.html I 2898 /remote.html OK | 

## Slide 77: Lab 6: Filesystem update
Open index1.html page
  Open your web browser
  In the address bar: <SPWF IP addr>/index1.html Type 192.168.x.1xx/index1.html
64

## Slide 78: Lab 6: Filesystem erase
Erase the external httpd filesystem
Type AT+S. HTTPDFSERASE
The files stored in the EXT FLASH memory will be erased
Tera Term output
Let's list the files
Type AT+S.FSL
65
All | 
I 461 /input_demo.shtml I 180 /message.shtml I 384 /output_demo.html I 614 /index.html I 157 /peers.shtml I 193 /config.shtml I 174 /status.shtml I 212 /404.html I 2022 /firstset.html I 2898 /remote.html OK | 

## Slide 79
Proceed to the next LAB!

## Slide 80: Lab 7: Socket interface
Objective
  Open TCP/UDP connection
  Write data to socket
  Read data from socket
  Close socket
Prerequisites
  Work alone
67
TCP/UDP socket
Socket Client
Socket Server

## Slide 81: Lab 7: TCP/UDP/UART socket interface
68
The Socket interface allows communication via TCP, UDP and UART. The SPWF is both a client and a server socket. In this LAB, will be detailed the socket client feature.
Host
End Product
Open TCP/UDP connection
Write data to socket
Read data from socket
Close socket

## Slide 82: Lab 7: Open TCP/UDP connection
The SOCKON command allows to open a TCP/UDP connection
to a specified host (up to 8 socket connections at same time).
Sintax
  AT+S.SOCKON=<hostname>,<port>,<protocol>,ind
Configuration parameters
  <hostname>: target host. DNS resolvable name or IP address
  <port>: TCP/UDP socket port
  <protocol>: t for TCP socket, u for UDP socket
  ind: indicate when data has arrived (optional). Up to 4 (x730 bytes) consecutive “Pending data” message (without any AT+S.SOCKR) are guaranteed. It is suggested to empty the buffer using the AT+S.SOCKR command and to avoid exceeding 4 indications.
69

## Slide 83: Lab 7: Open TCP/UDP connection
Open the TCP socket server (disable the firewall to properly run it)
  Folder ../hands_on_wifi/tcp socket server/server.exe
The TCP server listens for incoming connections on the port 32000. It sends back all data received.
70

## Slide 84: Optional - Lab 7: Open TCP/UDP connection
Using an Android platform, the socket server can be opened using a specific APP (Socket Protocol, available on Play Store)
The TCP socket server can be configured to listen for
incoming connections on the port 32000.
  Type 32000 on «Port Listen to» box
  Click on Listen
71

## Slide 85: Lab 7: Open TCP/UDP connection
• Type AT+S.SOCKON=192.168.0.10x,32000,t,ind
The client and the server use the socket identifier (ID)
displayed
72
Tera Term output
All | 
ID: 00 OK | 

## Slide 86: Lab 7: Write data to socket
The SOCKW command allows to write data to the specified ID
socket.
This command accepts data after the <cr> at the end of the command line.
Sintax
  AT+S.SOCKW=<ID>,<len>
Configuration parameters
  <ID>: socket identifier
  <len>: data length to send
73

## Slide 87: Lab 7: Write data to socket
Write data
  Type AT+S.SOCKW=00,13
Type hello world<CR>
SPWF shows that there are <pending data> and their amount
74
All
+WIND:55:Pending Data:0:13
Tera Term output
ID
Pending bytes
Note: the module is waiting 13 bytes to be written to the socket. As soon as 13 bytes (or characters) are sent from the terminal, the module is going to write them to the socket and will be ready to receive new commands.

## Slide 88: Lab 7: Read data from socket
The SOCKR command allows to read data from socket.
Sintax
  AT+S.SOCKR=<ID>,<len>
Configuration parameters
  <ID>: socket identifier
  <len>: data length to read
75

## Slide 89: Lab 7: Read data from socket
Read data
  Type AT+S.SOCKR=00,13
76
Tera Term output
All | 
hello world OK | 

## Slide 90: Lab 7: Close socket
The SOCKC command allows to close socket.
Sintax
  AT+S.SOCKC=<ID>
Configuration parameters
  <ID>: socket identifier
77

## Slide 91: Lab 7: Close socket
Tera Term output
Close socket
  Type AT+S.SOCKC=00
78
All | 
OK | 

## Slide 92
Proceed to the next LAB!

## Slide 93: Lab 8: MiniAP mode for the first set
Objective
  Create a direct connection between the module and an end device
  First set of the module in order to enable the connection between the module and a generic AP
Prerequisites
  Work alone
80

## Slide 94: Lab 8: Configuring the module in MiniAP mode
Tera Term output
The Mini AP mode is available starting from the following FW release:
SPWF01S-131115-de4568d-RELEASE
In order to set the module in Mini AP mode, the following parameters are needed
Set the SSID
  Type AT+S.SSIDTXT=SPWF_AP
Set the network privacy mode (0=OPEN or 1=WEP are supported)
  Type AT+S.SCFG=wifi_priv_mode,0
Set the network mode (1 = STA, 2 = IBSS, 3 = MiniAP)
  Type AT+S.SCFG=wifi_mode,3
81
All | 
OK | 

## Slide 95: Lab 8: Configuring the module in MiniAP mode
Save the settings on the flash memory and reset the module
  Type AT&W
  Type AT+CFUN=1
Tera Term output
82
SPWF_AP
All | 
+WIND:0:Console active +WIND:32:WiFi Hardware Started +WIND:26:WiFi Started AP +WIND:24:WiFi Up: 172.18.151.1 | 

## Slide 96
Lab 3: Configuring the module in MiniAP mode (WEP Key)
Configure the module using the WEP key (2 possible combinations
available)
Sample table:
83
AP configuration | AT command to be used
Security Mode: WEP WEP Key Length: 64 bit (10 hex digits) Authentication: Open Wep Key 1: 1234567890 | i.e. at+s.ssidtxt=SPWF_AP AT+S.SCFG=wifi_wep_keys[0],1234567890 AT+S.SCFG=wifi_wep_key_lens,05 AT+S.SCFG=wifi_auth_type,0 AT+S.SCFG=wifi_priv_mode,1 AT+S.SCFG=wifi_mode,3 at&w at+cfun=1
AP configuration | AT command to be used
Security Mode: WEP WEP Key Length: 128 bit (26 hex digits) Authentication: Open Wep Key 1: 123456789012345678 90123456 | i.e. at+s.ssidtxt=SPWF_AP AT+S.SCFG=wifi_wep_keys[0],12345678 901234567890123456 AT+S.SCFG=wifi_wep_key_lens,0D AT+S.SCFG=wifi_auth_type,0 AT+S.SCFG=wifi_priv_mode,1 AT+S.SCFG=wifi_mode,3 at&w at+cfun=1

## Slide 97
Lab 3: Configuring the module in MiniAP mode (WEP Key)
Notes:
“wifi_wep_key_lens” variable values: 05 and 0D
It’s possible to enter any text string as WEP key. It have to be converted into a hexadecimal key using the ASCII values of the characters. A maximum of 5 text characters can be entered for 64 bit keys, and a maximum of 13 characters for 128 bit keys.
In this case, it needs to manually convert your ASCII password to HEX and complete the wifi_wep_keys[0] variable with the HEX value.
i.e.
WEP key: test1
ASCII to HEX: 74:65:73:74:31
So, the AT command is: AT+S.SCFG=wifi_wep_keys[0],7465737431
84

## Slide 98: Lab 8: Mini AP mode
Associate your end device to the SPWF_AP network
  Find the SPWF_AP network and connect the end device to the module
85
SPWF_AP
Tera Term output
All | 
+WIND:28:90:18:7C:96:0D:0B Associated +WIND:29:DHCP reply for 172.18.151.2/90:18:7C:96:0D:0B to 172.18.151.2 +WIND:29:DHCP reply for 172.18.151.2/90:18:7C:96:0D:0B to 172.18.151.2 | 

## Slide 99: Lab 8: Mini AP mode
Open your web browser
In the address bar, type captiveportal.net
86
SPWF_AP
Tip: The Mini AP domain can be set using the variable ip_apdomainname.
The default value is “captiveportal.net”.
The Mini AP default homepage can be set using the variable ip_apredirect.
The default value is “firstset.html”.
Tip: If the AP domain name is not quickly opened, it’s suggested to turn off an eventual proxy server (check the connection settings or browser preferences)

## Slide 100: Lab 8: First Set Page
The first set page allows to configure the module in IDLE mode, STATION mode, IBSS mode and MINI AP mode.
87
Used for STA (if DHCP = OFF), IBSS
(mandatory), MINI AP (if DHCP = OFF)
Mandatory for IDLE, STA, IBSS, MINI AP |  | 
Used for STA, IBSS, MINI AP |  | 
Used for STA, IBSS (WEP), MINI AP (WEP) |  | 
Used for STA, IBSS (mandatory DHCP = OFF), MINI AP
Used for STA (WEP key), IBSS (WEP), MINI AP (WEP)
Used for STA, IBSS, MINI AP

## Slide 101: Lab 8: Mini AP mode
Set all the parameters required in order to enable the connection between the module and a generic AP
i.e. AP configured in WPA/WPA2 mode
MiniAP PassKey: anonymous (by default)
SSID of the access point
Password of the access point
Authentication type of the access point
Use mode of the module
88
Tip: The Mini AP PassKey can be set using
the variable “user_desc”.
The default value is “anonymous”.
Note: It’s suggested to configure SSID and password without special characters. If it needs to configure SSID and password containing special chars, bypass the “First Config” page and directly insert the whole URL in the browser URL bar.
Please note that also using this trick, some special chars will not be correctly sent (it may depend on the web browser used).
For example if the password is {helloworld}, use directly the following URL:
http://captiveportal.net/firstset.cgi?KEY=anonymous&SSID=ciscosb2&PWD={ helloworld}&Auth=2&Mode=1&confirm=GO
!

## Slide 102: Lab 8: Mini AP mode
Click on GO! button and then send the
parameters confirming with OK
89
AP
SSID: ciscosb2
SPWF_AP

## Slide 103: Lab 8: Mini AP mode
The module will receive the parameters and will automatically connect to the access point required
90
Tera Term output
ciscosb2
AP
All | 
+WIND:57:Received SSID is ciscosb2 +WIND:57:Received PWD is ********** +WIND:57:Received Auth mode is 2 +WIND:57:Received Mode is 1 +WIND:2:RESET +WIND:1:Poweron (******-*******-SPWF01S) +WIND:13:ST IWM: Copyright (c) 2012-2013 STmicroelectronics +WIND:3:Watchdog Running +WIND:0:Console active +WIND:46:WPA: Crunching PSK... +WIND:32:WiFi Hardware Started +WIND:21:WiFi Scanning +WIND:35:WiFi Scan Complete (0x0) +WIND:19:WiFi Join: 02:62:1F:51:8F:0B +WIND:25:WiFi Association with 'ciscosb2' successful +WIND:51:WPA Handshake Complete +WIND:24:WiFi Up: 192.168.1.106 | 

## Slide 104
Proceed to the next LAB!

## Slide 105: Lab 9: Socket interface - MiniAP mode
Objective
  Create a direct connection between the module and an end device
  Socket interface used in MiniAP mode
Prerequisites
  Work alone
92

## Slide 106: Lab 9: Configuring the module in MiniAP mode
Tera Term output
The Mini AP mode (available starting from the SPWF01S-131115- de4568d-RELEASE) also allows to use the socket interface. The procedure is the same as in Lab 7.
In order to set the module in Mini AP mode, the following parameters are
needed
Set the SSID
  Type AT+S.SSIDTXT=SPWF_AP
Set the network privacy mode
  Type AT+S.SCFG=wifi_priv_mode,0
Set the network mode (1 = STA, 2 = IBSS, 3 = MiniAP)
  Type AT+S.SCFG=wifi_mode,3
93
All | 
OK | 

## Slide 107: Lab 9: Configuring the module in MiniAP mode
Save the settings on the flash memory and reset the module
  Type AT&W
  Type AT+CFUN=1
Tera Term output
94
SPWF_AP
All | 
+WIND:0:Console active +WIND:32:WiFi Hardware Started +WIND:26:WiFi Started AP +WIND:24:WiFi Up: 172.18.151.1 | 

## Slide 108: Lab 9: Mini AP mode
Connect your PC to the SPWF_AP network
  Find the SPWF_AP network and connect the end device to the module
95
SPWF_AP
Tera Term output
All | 
+WIND:28:90:18:7C:96:0D:0B Associated +WIND:29:DHCP reply for 172.18.151.2/90:18:7C:96:0D:0B to 172.18.151.2 +WIND:29:DHCP reply for 172.18.151.2/90:18:7C:96:0D:0B to 172.18.151.2 | 

## Slide 109: Lab 9: Open TCP/UDP connection
As described in the Lab 7, the SOCKON command allows to
open a TCP/UDP connection to a specified host.
Sintax
  AT+S.SOCKON=<hostname>,<port>,<protocol>,ind
Configuration parameters
  <hostname>: target host. DNS resolvable name or IP address
  <port>: TCP/UDP socket port
  <protocol>: t for TCP socket, u for UDP socket
  ind: indicate when data has arrived (optional). Up to 4 consecutive “Pending data” message (without any AT+S.SOCKR) are guaranteed. It is suggested to empty the buffer using the AT+S.SOCKR command and to avoid exceeding 4 indications.
96

## Slide 110: Lab 9: Open TCP connection
Open the TCP socket server (disable the firewall to properly run it)
  Folder ../hands_on_wifi/tcp socket server/server.exe
The TCP server listens for incoming connections on the port 32000. It sends back all data received.
97

## Slide 111: Lab 9: Open TCP connection
• Type AT+S.SOCKON=172.18.151.2,32000,t,ind
Tera Term output
The client and the server use the socket identifier (ID) displayed
98
All | 
ID: 00 OK | 

## Slide 112: Lab 9: Write data to socket
The SOCKW command allows to write data to the specified ID
socket.
This command accepts data after the <cr> at the end of the command line.
Sintax
  AT+S.SOCKW=<ID>,<len>
Configuration parameters
  <ID>: socket identifier
  <len>: data length to send
99

## Slide 113: Lab 9: Write data to socket
Write data
  Type AT+S.SOCKW=00,13
Type hello world<CR>
SPWF shows that there are <pending data> and their amount
100
All
+WIND:55:Pending Data:0:13
Tera Term output
ID
Pending bytes
Note: the module is waiting 13 bytes to be written to the socket. As soon as 13 bytes (or characters) are sent from the terminal, the module is going to write them to the socket and will be ready to receive new commands.

## Slide 114: Lab 9: Read data from socket
The SOCKR command allows to read data from socket.
Sintax
  AT+S.SOCKR=<ID>,<len>
Configuration parameters
  <ID>: socket identifier
  <len>: data length to read
101

## Slide 115: Lab 9: Read data from socket
Read data
  Type AT+S.SOCKR=00,13
102
Tera Term output
All | 
hello world OK | 

## Slide 116: Lab 9: Close socket
The SOCKC command allows to close socket.
Sintax
  AT+S.SOCKC=<ID>
Configuration parameters
  <ID>: socket identifier
103

## Slide 117: Lab 9: Close socket
Tera Term output
Close socket
  Type AT+S.SOCKC=00
104
All | 
OK | 

## Slide 118
Proceed to the next LAB!

## Slide 119: Lab 10: Web server - MiniAP mode
Objective
  Create a direct connection between the module and an end device
  Web server used in MiniAP mode
Prerequisites
  Work alone
106

## Slide 120: Lab 10: Configuring the module in MiniAP mode
Tera Term output
The Mini AP mode (available starting from the SPWF01S-131115- de4568d-RELEASE) also allows to use the module file system (both RAM and Int/Ext FLASH).
In order to set the module in Mini AP mode, the following parameters are
needed
Set the SSID
  Type AT+S.SSIDTXT=SPWF_AP
Set the network privacy mode
  Type AT+S.SCFG=wifi_priv_mode,0
Set the network mode (1 = STA, 2 = IBSS, 3 = MiniAP)
  Type AT+S.SCFG=wifi_mode,3
107
All | 
OK | 

## Slide 121: Lab 10: Configuring the module in MiniAP mode
Save the settings on the flash memory and reset the module
  Type AT&W
  Type AT+CFUN=1
Tera Term output
108
SPWF_AP
All | 
+WIND:0:Console active +WIND:32:WiFi Hardware Started +WIND:26:WiFi Started AP +WIND:24:WiFi Up: 172.18.151.1 | 

## Slide 122: Lab 10: Mini AP mode
Connect your PC to the SPWF_AP network
  Find the SPWF_AP network and connect the end device to the module
109
SPWF_AP
Tera Term output
All | 
+WIND:28:90:18:7C:96:0D:0B Associated +WIND:29:DHCP reply for 172.18.151.2/90:18:7C:96:0D:0B to 172.18.151.2 +WIND:29:DHCP reply for 172.18.151.2/90:18:7C:96:0D:0B to 172.18.151.2 | 

## Slide 123: Lab 10: Access to Web server - Mini AP mode
Open your web browser
In the address bar, type
captiveportal.net/index.html
The SPWF01S homepage will be
displayed
110
SPWF_AP
Tip: The Mini AP domain can be set using the
variable ip_apdomainname.
The default value is “captiveportal.net”.

## Slide 124: Lab 10: Access to Web server - Mini AP mode
Open the SPWF01S Device Status
  click on the highlighted link
The SPWF01S Device Status will be
displayed
111
SPWF_AP
Tip: The Mini AP domain can be set using the variable
ip_apdomainname.
The default value is “captiveportal.net”.
The Mini AP default homepage can be set using the variable ip_apredirect.
The default value is “firstset.html”.

## Slide 125
Proceed to the next LAB!

## Slide 126: Lab 11: Remotely control - GPIOs
Objective
  write remotely a GPIO
  configure remotely a GPIO
  read remotely a GPIO
Prerequisites
  module connected to the AP or module configured in MiniAP mode
113

## Slide 127: Lab 11: Remotely control - GPIO
This feature allows to remotely write, configure and read a GPIO.
The module should be connected to the AP (as shown in Lab 3) or should be configured in Mini AP mode (as shown in Lab 8).
The external client have to open the remote.html page stored in the
module.
114
ENG-WPA
AP
SPWF_AP
AP

## Slide 128: Lab 11: Joining a network
Tera Term output
In order to be connected to an available Wifi network, the AP parameters setting is needed.
Set the SSID
  Type AT+S.SSIDTXT=ENG-WPA
Set the password
  Type AT+S.SCFG=wifi_wpa_psk_text,helloworld
Set the network privacy mode (0=none, 1=WEP, 2=WPA-Personal (TKIP/AES) or WPA2-Personal (TKIP/AES))
  Type AT+S.SCFG=wifi_priv_mode,2
Set the network mode (1 = STA, 2 = IBSS, 3 = MiniAP)
  Type AT+S.SCFG=wifi_mode,1
115
All | 
OK | 

## Slide 129: Lab 11: Joining a network
Save the settings on the flash memory and reset the module
  Type AT&W
  Type AT+CFUN=1
Tera Term output
116
ENG-WPA
AP
All | 
+WIND:0:Console active +WIND:46:WPA: Crunching PSK... +WIND:32:WiFi Hardware Started +WIND:21:WiFi Scanning +WIND:35:WiFi Scan Complete (0x0) +WIND:19:WiFi Join: 14:D6:4D:24:36:00 +WIND:25:WiFi Association with 'ENG-WPA' successful +WIND:51:WPA Handshake Complete +WIND:24:WiFi Up: 192.168.0.1xx | 

## Slide 130: Lab 11: Remotely control in MiniAP mode - GPIO
Open your web browser
In the address bar, type
192.168.x.1xx/remote.html
117
AP
ENG-WPA

## Slide 131: Lab 11: Remotely control in MiniAP mode - GPIO
Try to write the GPIO14 connected to the LED3 (check if the LED3 is mounted on your EVAL BOARD, otherwise can be used the GPIO13)
Click on the «GO!» button
and LED3 will switch on
118
AP
ENG-WPA

## Slide 132
Proceed to the next LAB!

## Slide 133: Lab 12: Input demo
Objective
  Send a message from the server (wifi module) to an external client connected to the same network
Prerequisites
  module connected to the AP or module configured in MiniAP mode
120

## Slide 134: Lab 12: Input demo
The module provides some DEMOs to show the interaction between the module and an external client connected to the same network.
The module should be connected to the AP (as shown in Lab 3) or should be configured in Mini AP mode (as shown in Lab 8).
In order to run this demo, the client have to open the
input_demo.shtml page stored in the module.
121
ENG-WPA
AP
SPWF_AP
AP

## Slide 135: Lab 12: Joining a network
Tera Term output
In order to be connected to an available Wifi network, the AP parameters setting is needed.
Set the SSID
  Type AT+S.SSIDTXT=ENG-WPA
Set the password
  Type AT+S.SCFG=wifi_wpa_psk_text,helloworld
Set the network privacy mode (0=none, 1=WEP, 2=WPA-Personal (TKIP/AES) or WPA2-Personal (TKIP/AES))
  Type AT+S.SCFG=wifi_priv_mode,2
Set the network mode (1 = STA, 2 = IBSS, 3 = MiniAP)
  Type AT+S.SCFG=wifi_mode,1
122
All | 
OK | 

## Slide 136: Lab 12: Joining a network
Save the settings on the flash memory and reset the module
  Type AT&W
  Type AT+CFUN=1
Tera Term output
123
ENG-WPA
AP
All | 
+WIND:0:Console active +WIND:46:WPA: Crunching PSK... +WIND:32:WiFi Hardware Started +WIND:21:WiFi Scanning +WIND:35:WiFi Scan Complete (0x0) +WIND:19:WiFi Join: 14:D6:4D:24:36:00 +WIND:25:WiFi Association with 'ENG-WPA' successful +WIND:51:WPA Handshake Complete +WIND:24:WiFi Up: 192.168.0.1xx | 

## Slide 137: Lab 12: Input demo
Open your web browser
In the address bar, type
192.168.x.1xx/input_demo.shtml
Insert the message to the client
i.e. type «test» (suggested – copy the string and paste it in the terminal) and then send a carriage
return
124
VERY IMPORTANT:
Both client and server are pending (2 sec) after the page request. If no message is sent from the module, a timeout mechanism will be triggered
!
The server shows the “+WIND:56 message”, and it will wait for a string to be inserted, and terminated by "[Cr]".
“+WIND:56:Insert message to client:%d”  %d is the Nth input SSI into html page (please refer to CGI&SSI Application Notes for details)
!

## Slide 138: Lab 12: Input demo
The module receives the HTML page containing the string inserted server-side.
Below this string, there are two buttons to try again the demo or to return to the homepage
125

## Slide 139
Proceed to the next LAB!

## Slide 140: Lab 13: Socket Server functionality
Objective
  Configure a Server Listening Port
  Open a TCP connection from a socket client to the module
  Data mode/Command Mode usage
Prerequisites
  module connected to the AP or module configured in MiniAP mode
  PC to be used as socket client
127
TCP socket
Socket Server
Socket Client

## Slide 141: Lab 13: Socket Server
This feature allows to enable the socket server mode. The module
can be able to listen for an incoming connection on the specified port.
The module should be connected to the AP (as shown in Lab 3) or should be configured in Mini AP mode (as shown in Lab 8).
Please refer to “Socket Server Application Notes” for more details.
128
ENG-WPA
AP
SPWF_AP
AP

## Slide 142: Lab 13: Joining a network
Tera Term output
In order to be connected to an available Wifi network, the AP parameters setting is needed.
Set the SSID
  Type AT+S.SSIDTXT=ENG-WPA
Set the password
  Type AT+S.SCFG=wifi_wpa_psk_text,helloworld
Set the network privacy mode (0=none, 1=WEP, 2=WPA-Personal (TKIP/AES) or WPA2-Personal (TKIP/AES))
  Type AT+S.SCFG=wifi_priv_mode,2
Set the network mode (1 = STA, 2 = IBSS, 3 = MiniAP)
  Type AT+S.SCFG=wifi_mode,1
129
All | 
OK | 

## Slide 143: Lab 13: Joining a network
Save the settings on the flash memory and reset the module
  Type AT&W
  Type AT+CFUN=1
Tera Term output
130
ENG-WPA
AP
All | 
+WIND:0:Console active +WIND:46:WPA: Crunching PSK... +WIND:32:WiFi Hardware Started +WIND:21:WiFi Scanning +WIND:35:WiFi Scan Complete (0x0) +WIND:19:WiFi Join: 14:D6:4D:24:36:00 +WIND:25:WiFi Association with 'ENG-WPA' successful +WIND:51:WPA Handshake Complete +WIND:24:WiFi Up: 192.168.0.1xx | 

## Slide 144: Lab 13: Socket Server
Socket server: turn ON the TCP Socket Server (user must specify the server listening port)
Type AT+S.SOCKD=32000
(AT+SOCKD=32000,u for UDP socket server)
Check the status of the socket server
  Type AT+S.STS=ip_sockd_port
131
ENG-WPA
Tera Term output
AP
All
OK
# ip_sockd_port = 32000
OK
Tip: you can Turn OFF the Socket Server using a server listening port = 0 (type AT+S.SOCKD=0)

## Slide 145: Lab 13: Socket Server
Socket client: can be used a simple socket client in order to test the communication (SocketTest – available on http://sourceforge.net/projects/sockettest)
132
AP
ENG-WPA

## Slide 146: Lab 13: Socket Server
Socket client:
  Insert the module’s IP Address and the port
  Click on Connect button
133
Tera Term output
All | 
+WIND:61:Incoming Socket Client:192.168.1.102 +WIND:60:Now in Data Mode | 

## Slide 147: Lab 13: Socket Server
The module (socket server) enters in data mode and a bidirectional channel is created to allow exchanging data with the socket client
Try to send and receive data from the module
134
Tera Term output
All | 
test_1 | 

## Slide 148: Lab 13: Socket Server – escape sequence
From Data Mode to Command Mode
  Configuration variable used: escape_seq (default is “at+s.”, case sensitive, suggested to be sent by the local host in a single complete packet with no CR or LF in the sequence)
Type at+s.
Now it’s possible to send AT commands while the socket connection
is still active
135
Tera Term output
Tip: During the Command Mode, you cannot send data to client, but can receive data from it. Every data chunk generates an URC (+WIND:64:Sockd Pending Data), with limit to 4 (x730 bytes). This is the max number of pending messages. From the 5th chunk on, messages are lost.
All | 
+WIND:59:Back to Command Mode | 

## Slide 149: Lab 13: Socket Server – return to data mode
From Command Mode to Data Mode
  While in Command Mode
Type AT+S.
(this is an AT command, AT+S. must be followed by <CR>)
The module returns in data mode
136
Tera Term output
AP
ENG-WPA
All | 
+WIND:60:Now in Data Mode | 

## Slide 150: Lab 13: Socket Server – turn off
Turn OFF the Socket Server
  Type at+s. (to enter in command mode)
  Type AT+S.SOCKD=0
137
Tera Term output
AP
ENG-WPA
All | 
OK +WIND:62:Socket Client Gone:192.168.1.102 | 

## Slide 151
Proceed to the next LAB!

## Slide 152: Lab 14: Low power modes
Objective
  Practice with Radio Power Save
  Sleep Mode
  Standby Mode
Prerequisites
  module connected to the AP
139

## Slide 153: Lab 14: Low power modes
This feature allows to enable the low power states.
The module supports the “Radio Power Save” mode, the “Sleep” mode and the “Standby” mode.
The module should be connected to the AP (as shown in Lab 3) in
order to use the “Radio Power Save” mode.
Please refer to “SPWF01S Power Management Application Notes” for
more details.
140
ENG-WPA
AP
Low Power

## Slide 154: Lab 14: Joining a network
Tera Term output
In order to be connected to an available Wifi network, the AP parameters setting is needed.
Set the SSID
  Type AT+S.SSIDTXT=ENG-WPA
Set the password
  Type AT+S.SCFG=wifi_wpa_psk_text,helloworld
Set the network privacy mode (0=none, 1=WEP, 2=WPA-Personal (TKIP/AES) or WPA2-Personal (TKIP/AES))
  Type AT+S.SCFG=wifi_priv_mode,2
Set the network mode (1 = STA, 2 = IBSS, 3 = MiniAP)
  Type AT+S.SCFG=wifi_mode,1
141
All | 
OK | 

## Slide 155: Lab 14: Joining a network
Save the settings on the flash memory and reset the module
  Type AT&W
  Type AT+CFUN=1
Tera Term output
142
ENG-WPA
AP
Low Power
All | 
+WIND:0:Console active +WIND:46:WPA: Crunching PSK... +WIND:32:WiFi Hardware Started +WIND:21:WiFi Scanning +WIND:35:WiFi Scan Complete (0x0) +WIND:19:WiFi Join: 14:D6:4D:24:36:00 +WIND:25:WiFi Association with 'ENG-WPA' successful +WIND:51:WPA Handshake Complete +WIND:24:WiFi Up: 192.168.0.1xx | 

## Slide 156: Lab 14: Low power modes – Power Save
143
r
S
r
s
t-
Module Power State | STM32 | WLAN
Standby | Standby | Standby
Sleep | Stop | PS
Power Save | Run | P or Fa t PS
Active Rx | Run | Rx Idle / Rx Active
Active Tx | Run | Tx Active

## Slide 157: Lab 14: Low power modes – Power Save
By default, the module starts in ACTIVE mode.
Enable the Power Save Mode:
  Type at+s.scfg=wifi_powersave,1 (“wifi_powersave,2” enables the Fast-PS mode)
Enable the doze operational mode:
  Type at+s.scfg=wifi_operational_mode,11 (“wifi_operational_mode,12” enables the quiescent mode)
Choose the wake up mode:
Wake up every n. beacon (specified in the wifi_beacon_wakeup variable)
  Type at+s.scfg=wifi_listen_interval,0
  Type at+s.scfg=wifi_beacon_wakeup,1
OR
Wake up every n. beacon adaptively (specified in the wifi_beacon_wakeup variable)
  Type at+s.scfg=wifi_listen_interval,1
  Type at+s.scfg=wifi_beacon_wakeup,1
144
Tip: The Wifi Power Save (wifi_powersave,1) can also be quickly enabled using the command: AT+CFUN=2

## Slide 158: Lab 14: Low power modes – Power Save
Save the settings on the flash memory and reset the module
  Type AT&W
  Type AT+CFUN=1
The WIND:66 message related to Low Power Mode will be
displayed
145
Tera Term output
ENG-WPA
AP
Low Power
All | 
+WIND:1:Poweron (******-*******-SPWF01S) +WIND:13:ST SPWF01S IWM: Copyright (c) 2012-2014 STMicroelectronics, Inc. All rights Reserved. +WIND:3:Watchdog Running +WIND:0:Console active +WIND:32:WiFi Hardware Started +WIND:21:WiFi Scanning +WIND:35:WiFi Scan Complete (0x0) +WIND:19:WiFi Join: 02:62:1F:51:8F:0B +WIND:25:WiFi Association with 'IoT' successful +WIND:51:WPA Handshake Complete +WIND:24:WiFi Up: 192.168.1.104 +WIND:66:Low Power mode:1 | 

## Slide 159: Lab 14: Low power modes – Sleep Mode
146
Module Power State
STM32
WLAN
Standby
Standby
S
r
as
t-
Standby
P or F t PS
PS or Fast-PS
Sleep
Stop
Power Save
Run
Active Rx
Run
Rx Idle / Rx Active
Active Tx
Run
Tx Active

## Slide 160: Lab 14: Low power modes – Sleep Mode
In the Sleep Mode, the core STM32 is stopped
Enable the Sleep Mode:
  Type at+s.scfg=sleep_enabled,1
Enable the Power Save Mode:
  Type at+s.scfg=wifi_powersave,1 (“wifi_powersave,2” enables the Fast-PS mode)
Enable the doze operational mode:
  Type at+s.scfg=wifi_operational_mode,11 (“wifi_operational_mode,12” enables the quiescent mode)
Choose the wake up mode:
Wake up every n. beacon (specified in the wifi_beacon_wakeup variable)
  Type at+s.scfg=wifi_listen_interval,0
  Type at+s.scfg=wifi_beacon_wakeup,1
OR
Wake up every n. beacon adaptively (specified in the wifi_beacon_wakeup variable)
  Type at+s.scfg=wifi_listen_interval,1
  Type at+s.scfg=wifi_beacon_wakeup,1
147
Tip: The Wifi Sleep Mode (and wifi_powersave,1) can also be quickly enabled using the command: AT+CFUN=3

## Slide 161: Lab 14: Low power modes – Sleep Mode
Save the settings on the flash memory and reset the module
  Type AT&W
  Type AT+CFUN=1
The WIND:69 message related to Sleep Mode will be displayed
148
+WIND:1:Poweron (******-*******-SPWF01S)
+WIND:13:ST SPWF01S IWM: Copyright (c) 2012-2014
STMicroelectronics, Inc. All rights Reserved.
+WIND:3:Watchdog Running
+WIND:0:Console active
+WIND:32:WiFi Hardware Started
+WIND:21:WiFi Scanning
+WIND:35:WiFi Scan Complete (0x0)
+WIND:19:WiFi Join: 02:62:1F:51:8F:0B
+WIND:25:WiFi Association with 'IoT' successful
+WIND:51:WPA Handshake Complete
+WIND:24:WiFi Up: 192.168.1.104
+WIND:66:Low Power mode:1
+WIND:69:Going into DeepSleep
Tera Term output
All
ENG-WPA
AP
Low Power

## Slide 162: Lab 14: Low power modes – Sleep Mode
Wake STM32 up using the GPIO6
  Put the GPIO6 to 2.5V (jumper on JP2 as in the picture)
The WIND messages will be displayed
149
Tera Term output
All | 
+WIND:70:Resuming from DeepSleep +WIND:53:Wakeup (GPIO6 High) | 

## Slide 163: Lab 14: Low power modes – Sleep Mode
Put STM32 in sleep mode using the
GPIO6
  Go back the GPIO6 floating (remove jumper
- as default)
The WIND:69 message will be
displayed
150
Tera Term output
All | 
+WIND:69:Going into DeepSleep | 

## Slide 164: Lab 14: Low power modes – Sleep Mode
Wake STM32 up using the remote
page
  Connect a device to the same module’s
network
  Open the following link: http://[module_IP_address]/remote.html
  Select “Wake” and click on “Go!” button
to wake up the module
The WIND message will be displayed
151
Tera Term output
All | 
+WIND:70:Resuming from DeepSleep | 

## Slide 165: Lab 14: Low power modes – Sleep Mode
Put STM32 in sleep mode using the
remote page
  Connect a device to the same module’s
network
  Open the following link: http://[module_IP_address]/remote.html
  Select “Sleep” and click on “Go!” button
to put the module in sleep mode
The WIND message will be displayed
152
Tera Term output
All | 
+WIND:69:Going into DeepSleep | 

## Slide 166: Lab 14: Low power modes – Standby Mode
153
Module Power State | STM32 | WLAN
Standby | Standby | Standby
Sleep | Stop | PS or Fast-PS
Power Save | Run | PS or Fast-PS
Active Rx | Run | Rx Idle / Rx Active
Active Tx | Run | Tx Active

## Slide 167: Lab 14: Low power modes – Standby Mode
During the Standby Mode, both the STM32 and the Radio will be put in standby mode. The standby mode allows to achieve the lowest power consumption.
Enable the Standby Mode:
  Type at+s.scfg=sleep_enabled,0 (Sleep mode must be disabled)
  Type at+s.scfg=standby_enabled,1
  Please be sure that GPIO6 isn’t forced high
Set the standby time to wake up via RTC alarm:
  Type at+s.scfg=standby_time,15
154
Tip: The Wifi Standby Mode can also be quickly enabled using the command:
AT+CFUN=4

## Slide 168
After 15 seconds, the module will be rebooted and will return in the ACTIVE state.
Lab 14: Low power modes – Standby Mode |  | 155
Save the settings on the flash memory and reset the module |  | 
Type AT&W |  | 
Type AT+CFUN=1 | Tera Term output | 
All | 
+WIND:0:Console active +WIND:32:WiFi Hardware Started +WIND:38:WiFi: Powered Down +WIND:67:Going into Standby:15 +WIND:68:Resuming from Standby +WIND:1:Poweron (******-*******-SPWF01S) +WIND:13:ST SPWF01S IWM: Copyright (c) 2012-2014 STMicroelectronics, Inc. All rights Reserved. +WIND:3:Watchdog Running +WIND:0:Console active +WIND:32:WiFi Hardware Started +WIND:21:WiFi Scanning +WIND:35:WiFi Scan Complete (0x0) +WIND:19:WiFi Join:02:62:1F:51:8F:0B +WIND:25:WiFi Association with 'IoT' successful +WIND:51:WPA Handshake Complete +WIND:24:WiFi Up:192.168.1.113 | 

## Slide 169: Lab 14: Low power modes – Standby Mode
Wake up the module using the GPIO6
Enable the Standby Mode:
  Type at+s.scfg=sleep_enabled,0 (make sure that Sleep mode is disabled)
  Type at+s.scfg=standby_enabled,1
  Type AT&W
  Type AT+CFUN=1
Put the GPIO6 to 2.5V to wake up the module
The WIND message will be displayed and
the module will return in ACTIVE state
Tera Term output
156
All | 
+WIND:68:Resuming from Standby +WIND:1:Poweron (******-*******- SPWF01S) ……… | 

## Slide 170
Proceed to the next LAB!

## Slide 171: Lab 15: STA/MINI AP switcher
Objective
  HW “STA to MiniAP” switcher
Prerequisites
  Work alone
158

## Slide 172: Lab 15: STA/MINI AP switcher
This feature allows to force the module in Mini AP mode starting from
a preexistent state.
“Recovery Mode”: this functionality could be useful to lead the module
in a known state and to reconfigure it (i.e. using the firstset page).
The GPIO7 will be used to drive this feature.
159

## Slide 173: Lab 15: STA/MINI AP switcher
Press and hold the SW2 button on the EVAL and then perform a reset (HW reset via SW1 button or SW reset via AT command)
Release the SW2 button
The MiniAP mode will be started and the module is discoverable with the following SSID:
  iwm-XX-YY-ZZ where XX-YY-ZZ are the last
six digits of module’s MAC ADDRESS
160
Tera Term output
Tip: To exit from “miniAP mode via
GPIO7”, perform a module’s reset
All | 
+WIND:2:Reset +WIND:1:Poweron (******-*******- SPWF01S) +WIND:13:ST SPWF01S IWM: Copyright (c) 2012-2014 STMicroelectronics, Inc. All rights Reserved. +WIND:39:HW in miniAP mode (GPIO7 Low) +WIND:0:Console active +WIND:3:Watchdog Running +WIND:32:WiFi Hardware Started +WIND:26:WiFi Started AP +WIND:24:WiFi Up:172.31.255.1 | 

## Slide 174
Proceed to the next LAB!

## Slide 175: Lab 16: IBSS connection
Objective
  Create an IBSS network
Prerequisites
  Work alone
162

## Slide 176: Lab 16: Create an IBSS network
In an IBSS network, the SSID is chosen by the client device that
starts the network.
Module settings to create an IBSS network:
Set the IBSS SSID
  Type AT+S.SSIDTXT=ADHOC
Set the network privacy mode (0=OPEN or 1=WEP are supported)
  Type AT+S.SCFG=wifi_priv_mode,0
Set the network mode (2 = IBSS)
  Type AT+S.SCFG=wifi_mode,2
163
OK
All
All OK
Tera Term output

## Slide 177: Lab 16: Create an IBSS network
Set IP address, IP default gateway, IP DNS and IP netmask
  Type AT+S.SCFG=ip_ipaddr,192.168.y.1xx
  Type AT+S.SCFG=ip_gw,192.168.y.1
  Type AT+S.SCFG=ip_dns,192.168.y.1
  Type AT+S.SCFG=ip_netmask,255.255.255.0
Turn off the DHCP
  Type AT+S.SCFG=ip_use_dhcp,0
Tera Term output
164
All | 
OK | 

## Slide 178: Lab 16: Create an IBSS network
AD-HOC
Save the settings on the flash memory and reset the module
  Type AT&W
  Type AT+CFUN=1
Tera Term output
165
All | 
+WIND:0:Console active +WIND:32:WiFi Hardware Started +WIND:21:WiFi Scanning +WIND:35:WiFi Scan Complete (0x0) +WIND:19:WiFi Join: EE:33:CE:00:24:18 +WIND:25:WiFi Association with 'ADHOC' successful +WIND:51:WiFi Handshake Complete +WIND:24:WiFi Up: 192.168.1.3 | 

## Slide 179: Lab 16: Create an IBSS network
Associate the iOS device with the ADHOC network
166
AD-HOC
Tip: manual configuration of static TCP/IPv4 parameters is suggested using a PC or an Android device.
properties
I.e. PC TCP/IPv4 properties

## Slide 180: Lab 16: Create an IBSS network
Find your IP address
  Type AT+S.STS
Open Safari web browser
In the address bar, type
<SPWF IP address>/index.html
  Type 192.168.y.1xx/index.html
167
AD-HOC

## Slide 181
Proceed to the next LAB!

## Slide 182: Lab 17: BlueMIX
Objective
  Hardware set-up
  Software set-up
Prerequisites
  Work alone
4

## Slide 183: Setup & Demo Examples HW prerequisites
X-NUCLEO-IKS01A1
X-NUCLEO-IDW01M1
X-NUCLEO-NFC01A1
NUCLEO-F401RE
STM32Nucleo
(ARM M4 core)
Sensors
Wi-Fi
Dynamic NFC
+
+
+

## Slide 184: Setup & Demo Examples SW prerequisites
ST-LINK/V2-1 USB driver (Link)
ST-LINK/V2-1 firmware upgrade (Link)
FP-CLD-BLUEMIX1 (Link)
  Copy the .zip file content into a folder on your PC
  The package will contain source code example (Keil, IAR, System Workbench) based only on NUCLEO-F401RE
Chrome web browser (http://www.google.com/chrome/)
Serial line monitor (e.g. Termite, http://www.compuphase.com/software_termite.htm or Tera Term, https://ttssh2.osdn.jp/index.html.en)
One of the three supported IDE (IAR Embedded Workbench, ARM Keil MDK, System Workbench for STM32)

## Slide 185: FP-CLD-BLUEMIX1 Wi-Fi, NFC and sensors software for Cloud connectivity
Download & unpack
www.st.com
1
FP-CLD-BLUEMIX1
Select Function Pack:
2
3
FP-CLD-BLUEMIX1 package structure
Docs
BSP, HAL and drivers
NDEF, MQTT, Wi-Fi libraries
IBM Application example
4
5
Compile/Flash and Run the project
or simply drag & drop the binary file to the USB mass storage drive corresponding to the STM32 Nucleo board
.\FP-CLD-BLUEMIX1\Projects\Multi\Applications\MQTT-IBM\EWARM\STM32F401RE-Nucleo
6
Visualize sensors data
Chrome
Web browser
www.st.com/stm32ode
NFC-enabled smartphone

## Slide 186: Use NFC to open automatically Quick Start web page on Tablet/Mobile
ST’s demo application reads the 4 sensors on the X-NUCLEO-IKS01A1 expansion board every 2 seconds and posts a template of 13 { Name, Value } pairs (= 1 tuple-type + 12 readings) to the IBM Cloud using the IBM Bluemix client via the Wi-Fi module and the hotspot’s LTE network.
  HTS221 (Relative temperature and humidity) = 2 readings
  LPS25HB (MEMS pressure sensor) = 1 reading
  LSM6DS0 (MEMS 6-axis accelerometer & gyroscope) = 6 readings
  LIS3MDL (MEMS 3-axis magnetometer) = 3 readings

## Slide 187: Sensor Data Visualization
ST has on-going programs with IBM Cloud hosting/computing services, Microsoft Azure, and Amazon Web Services (AWS) to start.
The ST demo uses the IBM QuickStart visualization website to plot the sensor data vs. time with auto-scaling of the y-axis to the range of data. (The software is unaware of the units of the values.)
https://quickstart.internetofthings.ibmcloud.com/#/device/0080E1B4FA41/sensor/
MAC Address = 0080E1B4FA41
Parameter = A-Temperature

## Slide 188: Detailed Demonstrations

## Slide 189: Download Terminal Emulator
TeraTerm Pro is available (for free) at:
  http://download.cnet.com/Tera-Term/3000-20432_4-75766675.html
  Download “teraterm-4.89.exe’” (or later). Run it.
  (The current installer is in the “Wi-Fi Tools” subdirectory of the memory stick. )

## Slide 190: Download ST-Link
Download STSW-LINK004 “STM32 ST-Link utility” at:
  http://www.st.com/web/en/catalog/tools/PF258168
  Download the “stsw-link004.zip” file.
  Extract the installer.
  Run it.
  (The current “STM32 ST-Link Utility v3.8.0.exe” installer is in the “Wi-Fi Tools” subdirectory.)

## Slide 191: Download optional free Wi-Fi Tools
Download Metageek “InSSIDer” to display beacons in the lab.
  http://www.inssider.com/downloads/
  (The current “InSSIDer 4” “Windows” installer is in the “Wi-Fi Tools” subdirectory.)
  We will use this tool during the demos.
Download “Wireshark” to use your PC’s Wi-Fi as a “sniffer”.
  https://www.wireshark.org/#download
  (The current 2.0.0 “Windows 64-bit” installer is in the “Wi-Fi Tools” subdirectory.)
  You will use this tool to capture data frames with your PC.

## Slide 192: Summary of Tutorials
Tutorial #1 – mini AP (similar to Lab 8 in the “Training-Hands On”):
  (STM32F401 Wi-Fi VCOM driver is loaded on the IBM cloud demo system)
  Using TeraTerm, configure the SPWF01S as a miniAP with unique beacon.
  Observe and associate beacons on PC or cellphone. Associate.
  Mention Lab 3 illustrates configure the SPWF01S as a client STA
Tutorial #2 – GPIOs (similar to Lab 11 in the “Training-Hands On”):
  Use AT+S.GPIOW to enable/disable LED on the X-NUCLEO-IDW01M1
  Use AT+S.FSL to list the web pages in the internal flash file system
  Control the LED with remote.html webpage from browser on PC or cellphone
Tutorial #3 -- IBM cloud client (new, secure, & hot):
  Using ST-Link to load the IBM cloud demo
  Starting the demo and optionally configuring the SSID and password using TeraTerm
  Slide with an explanation of the POSTed data
  Slide with explanation that the MAC address is entered in the URL.
  Browse the QuickStart Webpage and visualize the data graphically.

## Slide 193: IBM Bluemix Project using IAR Embedded Work Bench
.\STM32CubeFunctionPack_BLUEMIX1_F4_V1.0.0\Projects\Multi\Applications\MQTT_IBM\EWARM\STM32F401RE-Nucleo\Project.eww

## Slide 194: ST X-NUCLEO-IDW01M1 VCOM driver in IAR EWARM
.\X-CUBE-WIFI1\STM32CubeExpansion_WIFI1_V1.0.0\Projects\Multi\Applications\WiFi_VCOM\EWARM\STM32F401RE-Nucleo\Project.eww

## Slide 195: Tutorial #1a: Loading the VCOM driver
Run STM32-Link Utility.
Select “Target” + “Connect”.
Select “Program…”
“Start Address” is 0x08000000.
Select “Project-VCOM-WiFi-STM32F401.bin” in the “NUCLEO-STM32F401 Binaries” subdirectory using “Browse” button.
Click “Start”

## Slide 196: Tutorial #1a: Loading the VCOM driver
Wait for green “Memory programmed…” message.
Select “Target” + “Disconnect”
Done!
Using Teraterm, on the PC, we will now access the SPWF01S module directly over the UART.

## Slide 197: Tutorial #1b: Configuring TeraTerm
Run TeraTerm.
Select “Setup” + “Serial Port…”
Set “Port: to the last COM port.
Set “Baud rate” to “115200”.
Click “OK”.

## Slide 198: Tutorial #1c: Configure the module to echo
Enter: “at”<cr>.
To enable character echo, enter: “at+s.scfg=localecho1,1”<cr>
Enter: “at”<cr>.
Enter: “at&v”<cr>.

## Slide 199: Tutorial #1d: Configure miniAP mode
Set the SSID to “SPWF_AP### “, where ### is the last 3 digits of the serial number of the serial number on the NUCLEO-STM32F401 card.
  Enter: “at+s.ssidtxt=SPWF_AP789”<cr>
Set the network privacy mode to open (0=open or 1=WEP).
  Enter: “at+s.scfg=wifi_priv_mode,0”<cr>
Set the network mode (1=client STA, 2=IBSS, or 3=miniAP).
  Enter: “at+s.scfg=wifi_mode,3”<cr>
Save the settings in flash memory.
  Enter: “at&w”<cr>
Do a software reset, so the
settings to take effect.
  Enter “at+cfun=1”<cr>

## Slide 200: Tutorial #1d: Configure miniAP mode
Verify the module is beaconing using the Wi-Fi menu on your cellphone, or the menu on the PC task bar, or inSSIDer. Associate with it.
Record the miniAP’s private IP address

## Slide 201: Tutorial #2a: Toggle GPIO14 LED3
Note that the Red LED3 on the X-NUCLEO-IDW01M1 board is off.
Configure GPIO14 as an output. Enter: “at+s.gpioc=14,out”<cr>
Turn the Red LED3 on. Enter: “at+s.gpiow=14,1”<cr>
Turn the Red LED off. Enter: “at+s.gpiow=14,0”<cr>
Repeat previous two steps ad nauseum.

## Slide 202: Tutorial #2b: Toggle GPIO14 LED3 with browser
Display all the files contained within the module internal flash file system. Do a file system list:
  Enter “at+s.fsl”<cr>
The browser running on the client STA (cellphone or PC) will read the remote.html file over-the-air and control LED3 over-the-air.

## Slide 203: Tutorial #2b: Toggle GPIO14 LED3 with browser
Your cellphone or PC is associated as a miniAP as in Tutorial #1d.
Recall the module’s IP address which was displayed by its DHCP server in the “+WIND:24:WiFi Up:” message when the module rebooted.

## Slide 204: Tutorial #2b: Toggle GPIO14 LED3 with browser
Direct the browser on the client STA to “172.xxx.yyy.1/remote.html”
Under “SPWF01 Remote GPIOs, change the radio button to “Write”, and the “Number and Value:” fields to “14” and “High”.
Click on “Go!”, and note that the GPIO14 LED3 goes On.
Change the radio button to “Write”, and the “Number and Value:” fields to “14” and “Low”.
Click on “Go!”, and note LED3 goes Off. Repeat ad infinitum.

## Slide 205: Tutorial #3b: Configure Credentials
The IBM Cloud Demo firmware runs in client STA mode.
The IBM Cloud Demo firmware includes the IBM Bluemix client SW.
When it starts, it asks for the credentials of an AP to access the Internet, through the Wi-Fi module, in order to post sensor data to the IBM Cloud. You can select the SSID, Passphrase, and security type (open, WEP, or WPA/WPA2).
The default credentials for the IBM cloud demo are: SSID = “STM”; Passphrase = “STMdemoPWD”; and Security type = WPA/WPA2-Personal.
As a client STA, the SPWF01S module supports WPA2-Personal security, but not WPA2-Enterprise. The SPWF04S module will not be limited in this way.

## Slide 206: Tutorial #3: ST-IBM Cloud demo
End-to-end application to transmit sensors data to a cloud service based on IBM Bluemix, visualize them on a web page, and receive commands back to Nucleo
Nucleo based application
  HW : Nucleo + Sensors Board + Wi-Fi
  SW : application reading and transmitting in real time sensors data (temperature, pressure, humidity, motion) to IBM Bluemix. MQTT over TLS 1.2 is used as application protocol for secure data communication with Bluemix.
  Landing page to visualize data: https://quickstart.internetofthings.ibmcloud.com
  Unique page for a given MAC address

## Slide 207: Tutorial #3a: Load the IBM cloud demo
Run STM32-Link Utility.
Select “Target” + “Connect”.
Select “Program…”
“Start Address” is 0x08000000.
Select “v1.2-IBM-Quickstart-without NFC.bin” in the “NUCLEO-STM32F401 Binaries” subdirectory using “Browse” button.
Click “Start”

## Slide 208: Tutorial #3b: Configure Credentials
The IBM Cloud Demo firmware runs in client STA mode.
The IBM Cloud Demo firmware includes the IBM Bluemix client SW.
When it starts, it asks for the credentials of an AP to access the Internet, through the Wi-Fi module, in order to post sensor data to the IBM Cloud. You can select the SSID, Passphrase, and security type (open, WEP, or WPA/WPA2).
The default credentials for the IBM cloud demo are: SSID = “ST_OFFICE”; Passphrase = “stbrasil2016”; and Security type = WPA/WPA2-Personal.
As a client STA, the SPWF01S module supports WPA2-Personal security, but not WPA2-Enterprise. The SPWF04S module will not be limited in this way.
When visiting customers, to get around this issue and cases where non-authorized devices are not permitted on the corporate intranet, we travel with a hotspot when visiting customers, configured to the defaults.

## Slide 209: Tutorial #3c: MAC address identity
Note that the demo reports the MAC address of its Wi-Fi module.
This globally-unique identifier is used in the URL to access the IBM Cloud, so that the data from one demo board set can be distinguished from another, and is independent of IP address assigned by the AP’s DHCP server. Your data is stored securely (with HTTPS end-to-end security) without risk of being intermingled with others’ data.
Record the URL displayed for the visualization phase of the demo.

## Slide 210: Tutorial #3d: HTTP POST of sensor data
ST’s demo application reads the 4 sensors on the X-NUCLEO-IKS01A1 shield every 2 seconds and posts a template of 13 { Name, Value } pairs (= 1 tuple-type + 12 readings) to the IBM Cloud using the IBM Bluemix client via the Wi-Fi module and the hotspot’s LTE network.
  HTS221 (Relative temperature and humidity) = 2 readings
  LPS25HB (MEMS pressure sensor) = 1 reading
  LSM6DS0 (MEMS 6-axis accelerometer & gyroscope) = 6 readings
  LIS3MDL (MEMS 3-axis magnetometer) = 3 readings

## Slide 211: Tutorial #3d: Sensor Data Visualization
ST has on-going programs with IBM Cloud hosting/computing services, Microsoft Azure, and Amazon Web Services (AWS) to start.
The ST demo uses the IBM QuickStart visualization website to plot the sensor data vs. time with auto-scaling of the y-axis to the range of data. (The software is unaware of the units of the values.)
https://quickstart.internetofthings.ibmcloud.com/#/device/0080E1B4FA41/sensor/
MAC Address = 0080E1B4FA41
Parameter = A-Temperature

## Slide 212: FP-CLD-BLUEMIX1 WiFi, NFC and sensors software for Cloud connectivity
Download & unpack
www.st.com
1
FP-CLD-BLUEMIX1
Select
2
3
V-ODE-WEAR3 package structure
Docs
BSP, HAL and drivers
NDEF, MQTT, Wi-Fi libraries
IBM Application example
4
5
Compile/Flash and
Run the project
.\ FP-CLD-BLUEMIX1\Projects\Multi\Applications\MQTT-IBM\EWARM\STM32F401RE-Nucleo
NFC-enabled smartphone
6
Visualize sensors data
Chrome
Web browser

## Slide 213: References on www.st.com
NUCLEO-F401RE (STM32F401 mother board)
  http://www.st.com/web/catalog/tools/FM116/SC959/SS1532/LN1847/PF260000
X-NUCLEO-IDW01M1 (SWPF01SA Wi-Fi module shield)
  http://www.st.com/web/catalog/tools/FM146/CL2167/SC2006/LN1988/PF262207
  SPWF01SA Wi-Fi module
    http://www.st.com/web/catalog/sense_power/FM2185/SC1930/PF258591
  Wi-Fi module documentation
    http://www.st.com/web/catalog/sense_power/FM2185/SC1930
X-NUCLEO-IKS01A1 (Motion MEMS & environmental sensor shield)
  http://www.st.com/web/catalog/tools/FM146/CL2167/SC2006/LN1989/PF261191
  HTS221 (Relative temperature and humidity)
  LPS25HB (MEMS pressure sensor)
  LSM6DS0 (MEMS 6-axis accelerometer & gyroscope)
  LIS3MDL (MEMS 3-axis magnetometer)

## Slide 214: Symptom: ST-Link or IAR download tool experiences flakiness
Solution: Remove 0-ohm resistor R21. (R21 connects GPIO14 of the module to PA14 on the mother board.)
R21 will be removed in future batches of X-NUCLEO-IDW01M1. But distributors’ inventory may be stale. Boards at this training have been reworked. 
R21

## Slide 215: JP3/JP4 not mounted
Some boards are shipped without jumpers JP3 and JP4 mounted on pins 1-to-2. Today there are jumpers in the packaging.
Boards at the training have been reworked. Not critical.
JP3 to be mounted in position 1-2
(so mother board can control RESETn of Wi-Fi module)
JP4 to be mounted in position 1-2
(so mother board can control GPIO6 of Wi-Fi module)

## Slide 216: X-NUCLEO-IDW01M1 R21, JP3, & JP4

## Slide 217: Order Codes Summary
Modules
Evaluation Boards
Order code | Description
STEVAL-IDW001V1 | Daughter Board usable with STEVAL-PCC018V1 or with the STM32F0-Discovery
STEVAL-PCC018V1 | USB-UART Bridge
Order Code | Description
SPWF01SA.11 | 1MB Extended Flash, Integrated Antenna, AT Full Stack
SPWF01SC.11 | 1MB Extended Flash, Integrated U.fl. connector, AT Full Stack
SPWF01SA.21 | Integrated Antenna, AT Full Stack
SPWF01SC.21 | Integrated U.fl. connector, AT Full Stack
Public WiFi modules Forum on
https://my.st.com/public/STe2ecommunities/interface/Lists/WiFi Modules
X-Pansion
Order code | Description
X-NUCLEO-IDW01M1 | Wi-Fi evaluation board based on SPWF01SA module, to allow expansion of the STM32 NUCLEO mother boards

## Slide 218
THANK YOU!